## Slide 1
COMPUTER NETWORKS PROJECT
Design and Implementation of a
Secure Campus Network
Using Subnetting, VLANs, Routing, and Access Control Lists (ACL)
Student Name:
[Your Full Name]
Course / College:
[Course Name], [College Name]
Notes: Welcome the panel. State the project title clearly: a secure campus network using subnetting, VLANs, routing, and ACLs. Mention your name and course briefly, then move to the objective.

## Slide 2
Objective
What this project sets out to achieve
Design a Campus Network
Plan a scalable, structured network layout for the entire campus
Connect Three Departments
Integrate Admin, Academic, and Hostel blocks into one network
Ensure Secure Communication
Control traffic between departments using Access Control Lists (ACL)
Secure Campus Network Design
2
Notes: Explain that the goal is to design a working campus network that connects three departments — Admin, Academic, and Hostel — while making sure communication between them is controlled and secure using ACLs.

## Slide 3
Network Design
Basic topology connecting all campus departments
Router
Admin
Academic
Hostel
Data Flow
Each department has its own switch connecting all its PCs
Every switch connects up to the central router
Router forwards traffic between departments (inter-VLAN routing)
Router also connects the campus to the internet gateway
Secure Campus Network Design
3
Notes: Walk through the topology: each department has PCs connected to a switch, and all switches connect to a central router. The router handles traffic between departments (inter-VLAN routing) and can also connect to the internet.

## Slide 4
IP Addressing (Subnetting)
Each department gets its own subnet
Admin
Network Address
192.168.1.0 /24
192.168.1.1 – 192.168.1.254
Academic
Network Address
192.168.2.0 /24
192.168.2.1 – 192.168.2.254
Hostel
Network Address
192.168.3.0 /24
192.168.3.1 – 192.168.3.254
Purpose of Subnetting
Divides one large network into smaller, manageable sub-networks
Reduces broadcast traffic and improves overall network performance
Isolates departments so a problem in one does not affect others
Makes it easier to apply security rules (ACLs) per department
Secure Campus Network Design
4
Notes: Explain subnetting: each department is assigned its own /24 subnet (Admin 192.168.1.0/24, Academic 192.168.2.0/24, Hostel 192.168.3.0/24). This keeps broadcast traffic local and makes it easy to apply security rules per department.

## Slide 5
VLAN Configuration
Logical segmentation of the physical network
VLAN ID | Department | Subnet
VLAN 10 | Admin | 192.168.1.0/24
VLAN 20 | Academic | 192.168.2.0/24
VLAN 30 | Hostel | 192.168.3.0/24
Switch Configuration Example
vlan 10
name Admin
vlan 20
name Academic
vlan 30
name Hostel
interface fa0/1
switchport access vlan 10
Why Use VLANs?
Segmentation
Separates broadcast domains for Admin, Academic, and Hostel even on shared switches
Security
Users in one VLAN cannot directly see traffic from another VLAN
Flexibility
Devices can be grouped logically, regardless of their physical location
Secure Campus Network Design
5
Notes: Explain VLANs: VLAN 10 for Admin, VLAN 20 for Academic, VLAN 30 for Hostel. Even if devices share the same physical switch, VLANs logically separate their traffic for better security and easier management. Show the sample switch config if asked.

## Slide 6
Routing and Testing
Connecting departments and verifying communication
1
Router Connects All Networks
A single router performs inter-VLAN routing between Admin, Academic, and Hostel
2
Inter-Network Communication
Devices in different subnets can reach each other through the router
3
Testing with Ping (ICMP)
ping 192.168.2.1 is used from each subnet to check reachability
Observation
Ping tests show partial success — some paths reply normally, while others silently fail due to security rules applied later (ACL).
Ping Test Results
ping 192.168.1.1 (Admin)
from Academic PC
ping 192.168.3.1 (Hostel)
from Academic PC
ping 192.168.3.1 (Hostel)
from Admin PC
ping 192.168.1.1 (Admin)
from Hostel PC
Note: Hostel → Admin fails after ACL is applied (see next slide)
Secure Campus Network Design
6
Notes: Explain that the router connects all three VLANs and allows inter-network communication. Ping (ICMP) is used to test reachability between subnets. Note that before applying ACLs, all pings succeed; the 'partial success' happens once ACL rules are introduced next.

## Slide 7
Security Using ACL
Access Control List applied on the router interface
DENY
Hostel → Admin traffic
access-list 101 deny ip 192.168.3.0 0.0.0.255 192.168.1.0 0.0.0.255
PERMIT
Admin → Hostel traffic
access-list 101 permit ip 192.168.1.0 0.0.0.255 192.168.3.0 0.0.0.255
Applied on: Router interface facing Hostel VLAN (Fa0/3), direction: inbound
Result: One-Way Communication Achieved
Admin can reach Hostel, but Hostel cannot reach Admin — confirming the ACL successfully enforces one-directional, secure access between departments.
Secure Campus Network Design
7
Notes: Explain the ACL: it is applied on the router interface facing the Hostel VLAN. One rule blocks Hostel-to-Admin traffic, another explicitly permits Admin-to-Hostel traffic. Emphasize the outcome: one-way communication is achieved, which is a simple, real demonstration of network access control.